## Slide 1: Energy systems
PLCY-798K
February 8, 2023
Gokul Iyer

## Slide 2: Agenda for today
Importance of the energy system in integrated assessment modeling
Components of the energy system
Quick refreshers
  Scenarios
  International climate policy
  Energy technologies
Key characteristics of long-term energy system transformations
Modeling of non-economic factors
Cutting-edge research in modeling of energy systems in IAMs

## Slide 3: The energy system is at the heart of integrated assessment models…
3
Temperature, RF
Exogenous Assumptions
Population
Labor Productivity
Technology
Policy
Livestock
Crops & Forests
Electric & Refining
Primary Energy Supply
Economic Activity
Commodity Prices
Prices, Taxes, e.g. CO2
Outputs of IAMs
Resources
CO2, GHGs, aerosols, OGs
External Data
Economy
Energy
Agriculture & Land Use
Water
Climate

## Slide 4: ...because the energy system is at the heart of the climate problem…
Source: https://www.epa.gov/ghgemissions/global-greenhouse-gas-emissions-data

## Slide 5: Three main components of the energy system
Resources
(e.g. coal, gas, oil)
Conversion
(e.g. electricity)
Services
(e.g. heating, cooling)
Primary Energy
Secondary Energy
Final Energy
Energy Supply
Energy Demand

## Slide 6: Components of and processes in the energy system: Some details
Source: GEA, 2012

## Slide 7: Components of and processes in the energy system: Example starting with a fossil resource
Source: GEA, 2012

## Slide 8: Components of and processes in the energy system: Example starting with a ren resource
Source: GEA, 2012

## Slide 9: Global flow of energy in 2019
Source: IPCC, AR6

## Slide 10: Quick refresher #1: Scenarios

## Slide 11: IAMs are used to produce internally consistent “scenarios” or “pathways” of the future
Simply put, scenarios are conditional forecasts
Scenarios describe how the future may develop based on a coherent and internally consistent set of assumptions about key relationships and driving forces
if
then
11
Notes: IAMs contain structured relationships that can be used to produce conditional forecasts

## Slide 12: A few things to keep in mind about scenarios
Scenarios do not attach probabilities to the futures they describe and are not predictions nor forecasts of the future
  Rather, scenarios describe plausible future outcomes that provide a valuable point of reference to aide in analysis and/or decision making
Scenarios can be used in an explorative manner or for scientific assessment to understand interactions and linkages between key variables related to natural (e.g. land) and/or human (e.g. energy) systems of interest
Scenarios could also be used to elucidate strategies to address climate change or other issues of societal/policy interest
https://blog.commlabindia.com/elearning-design/scenario-based-elearning-assessments

## Slide 13: Quick refresher #2: International climate policy

## Slide 14: How much do we need to reduce global GHG emissions to implement Paris?
Holding the increase in the global average temperature to well below 2 °C above pre-industrial levels and to pursue efforts to limit the temperature increase to 1.5 °C above pre-industrial levels
The international community has established ambitious long-term goals

## Slide 15
100%

## Slide 16
How much should energy-system emissions be reduced?

## Slide 17
100% or more

## Slide 18: Scenarios produced by IAMs suggest emission increases in the absence of focused policies
GHG emissions in “No climate Policy” scenarios
Source: IPCC, AR5

## Slide 19: Scenarios based on IAMs that incorporate Paris goals are characterized by major emissions reductions in the energy system
GHG emissions in mitigation scenarios (dark) compared to emissions in baseline scenarios (light)
Source: IPCC, AR5

## Slide 20: Quick refresher #3: Energy technologies

## Slide 21: What kinds of energy technologies result in non-zero emissions?

## Slide 22: What kinds of energy technologies result in non-zero emissions?
Coal-fired power plants
Oil refineries, industries
Combustion engines
Building furnaces

## Slide 23: What kinds of energy technologies result in low- or zero- emissions?

## Slide 24: What kinds of energy technologies result in low- or zero- emissions?
Renewables
Biofuels
Carbon Capture Utilization & Storage
Nuclear
Hydrogen
Electric vehicles

## Slide 25: What kinds of energy technologies result in negative emissions?

## Slide 26: What kinds of energy technologies result in negative emissions?
https://www.globalccsinstitute.com/insights/authors/AliceGibson/2015/11/25/importance-bio-ccs-deliver-negative-emissions
Bioenergy + CCUS
Direct Air Capture

## Slide 27: Key questions of interest in the energy-climate problem that we will focus on today
What kinds of transitions need to occur in the energy system to achieve deep emissions reductions? What is the role of different energy technologies in these transitions?
What is the role of institutions in those transitions?

## Slide 28
What kinds of transitions need to occur in the energy system to achieve deep emissions reductions?
What is the role of different energy technologies in these transitions?

## Slide 29: Scenarios consistent with Paris goals are characterized by major scaling up of low carbon technologies
Source: IPCC, AR6
Boxes indicate 25th and 75th percentiles;
whiskers indicate 5th and 95th percentiles

## Slide 30: Scenarios consistent with Paris goals are characterized by decreases in fossil production and consumption
Source: IPCC, AR6
Boxes indicate 25th and 75th percentiles;
whiskers indicate 5th and 95th percentiles

## Slide 31: Scenarios consistent with Paris goals are characterized by increases in electricity and H2 in end-use sectors
Source: IPCC, AR6
Boxes indicate 25th and 75th percentiles;
whiskers indicate 5th and 95th percentiles

## Slide 32: Scenarios consistent with Paris goals are characterized by changes in investment patterns
Global average annual investments (2023–2052) [Billion USD/ yr]
Source: IPCC, AR6
Bars show median values across models-scenarios, and whiskers the interquartile ranges

## Slide 33: IAM based pathways toward net-zero emissions in the U.S. by 2050 suggest significant scaling up of investments compared to historical rates
U.S. Electric Generation Capacity Additions
Source:
U.S. LTS 2021

## Slide 34: Scenarios consistent with Paris goals are characterized by stranded assets
Mitigation could result in pre-mature write-downs, devaluations, and conversion to liabilities of carbon-intensive assets, referred to as “stranding” of assets.
In the context of climate change mitigation, stranded assets could manifest in various forms such as:
  Fossil-fuel resources that cannot be burned in order to maintain a long-term temperature goal
  Pre-mature retirement of carbon-intensive capital due to climate policies
https://www.greenbiz.com/article/state-green-business-stranded-assets

## Slide 35: Why are stranded assets important?
Stranded assets could create financial and political threats:
  Economic risks: Financial risks that could arise for parties that have suffered loss and damage from climate change mitigation.
  Political economy risks: Stranded assets create loss of wealth for few and could result in lobbying and rent-seeking behavior.
https://www.reminetwork.com/articles/climate-risk-raises-stranded-asset-potential/

## Slide 36: Globally, investments and stranded assets implications of Paris Agreement are non-trivial
Source: Iyer et al., 2015, The contribution of Paris to limit global warming to 2°C, Environmental Research Letters
Paris to 2°C
No Paris to 2°C
Least Cost 2°C
Capacity Additions and pre-mature retirements [GW/yr]
Current installed capacity globally is ~8000GW.
The Paris- and No Paris to 2°C scenarios suggest
pre-maturely retiring 20-25% of this capacity beyond 2030

## Slide 37: Globally, investments and stranded assets implications of Paris Agreement are non-trivial
Paris to 2°C
No Paris to 2°C
Least Cost 2°C
Capacity Additions and pre-mature retirements [GW/yr]
Stranded asset implications under 1.5°C would be even more prominent
Source: Iyer et al., 2015, The contribution of Paris to limit global warming to 2°C, Environmental Research Letters

## Slide 38: Looking beyond the energy system: IAM-based research suggests that achieving economy-wide net-zero emissions is a zero-sum game
Some non-CO2 emissions are hard to reduce (e.g. from cattle)
Carbon dioxide removal (CDR) will be critical to offset those emissions
The greater the scale of CDR, the lower is the level of mitigation of CO2 emissions from fossil fuels and industry and vice versa

## Slide 39: Example diagnostic scenarios based on GCAM

## Slide 40: Example using GCAM: Six Emissions Scenarios
Three technology assumptions
Full technology
No BioCCS
No CCS and Nuclear
Three assumptions about emissions in 2050 (Energy system CO2 only)
Decline slightly from 2020 to 2010 levels by 2050
Decline to 25% below 2010 levels in 2050
Decline to 50% below 2010 levels in 2050 (2⁰C Scenario)
Assumptions are consistent with literature

## Slide 41: Primary Energy: Reference Scenario
Full Technology Portfolio
No Nuclear and CCS
No Bio CCS
Chart: 
| 1990 | 1995 | 2000 | 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Oil | 136.5998 | 147.8861 | 159.1724 | 170.4588 | 176.0788 | 185.4799 | 184.4971 | 181.1828 | 178.9079 | 177.7472 | 178.9437 | 181.8681 | 186.3747
Natural Gas | 70.3394 | 79.8275 | 89.3156 | 98.8037 | 113.8448 | 127.4344 | 147.2497 | 172.5287 | 195.3516 | 214.9606 | 232.8845 | 247.7666 | 260.7587
Coal | 92.7774 | 103.3057 | 113.8341 | 124.3624 | 143.2598 | 168.6401 | 195.2937 | 228.6298 | 257.9224 | 284.3764 | 311.2991 | 336.3787 | 361.2122
Commercial Biomass | 13.3797 | 14.8309 | 16.282 | 17.7332 | 20.962 | 22.9203 | 33.9514 | 43.8312 | 54.6427 | 65.4709 | 75.3689 | 84.9915 | 94.3088
Nuclear | 7.246 | 8.1522 | 9.0584 | 9.9646 | 9.9226 | 10.8957 | 12.7667 | 14.6897 | 17.1774 | 20.1724 | 23.8595 | 27.6416 | 31.4095
Non-Biomass Renewables | 7.8662 | 8.9642 | 10.0621 | 11.16 | 13.9867 | 16.9541 | 20.2575 | 23.0763 | 26.3875 | 30.2539 | 33.577 | 37.1656 | 41.1038
Energy Reduction

## Slide 42: Primary Energy: 2010 Emissions
Full Technology Portfolio
No Nuclear and CCS
No Bio CCS
Chart: 
| 1990 | 1995 | 2000 | 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Oil | 136.5998 | 147.8861 | 159.1724 | 170.4588 | 176.0788 | 185.4799 | 184.4971 | 181.1828 | 178.9079 | 177.7472 | 178.9437 | 181.8681 | 186.3747
Natural Gas | 70.3394 | 79.8275 | 89.3156 | 98.8037 | 113.8448 | 127.4344 | 147.2497 | 172.5287 | 195.3516 | 214.9606 | 232.8845 | 247.7666 | 260.7587
Coal | 92.7774 | 103.3057 | 113.8341 | 124.3624 | 143.2598 | 168.6401 | 195.2937 | 228.6298 | 257.9224 | 284.3764 | 311.2991 | 336.3787 | 361.2122
Commercial Biomass | 13.3797 | 14.8309 | 16.282 | 17.7332 | 20.962 | 22.9203 | 33.9514 | 43.8312 | 54.6427 | 65.4709 | 75.3689 | 84.9915 | 94.3088
Nuclear | 7.246 | 8.1522 | 9.0584 | 9.9646 | 9.9226 | 10.8957 | 12.7667 | 14.6897 | 17.1774 | 20.1724 | 23.8595 | 27.6416 | 31.4095
Non-Biomass Renewables | 7.8662 | 8.9642 | 10.0621 | 11.16 | 13.9867 | 16.9541 | 20.2575 | 23.0763 | 26.3875 | 30.2539 | 33.577 | 37.1656 | 41.1038
Energy Reduction

## Slide 43: Primary Energy: 25% reduction
Full Technology Portfolio
No Nuclear and CCS
No Bio CCS
Chart: 
| 1990 | 1995 | 2000 | 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Oil | 136.5998 | 147.8861 | 159.1724 | 170.4588 | 176.0788 | 185.4799 | 184.4971 | 181.1828 | 178.9079 | 177.7472 | 178.9437 | 181.8681 | 186.3747
Natural Gas | 70.3394 | 79.8275 | 89.3156 | 98.8037 | 113.8448 | 127.4344 | 147.2497 | 172.5287 | 195.3516 | 214.9606 | 232.8845 | 247.7666 | 260.7587
Coal | 92.7774 | 103.3057 | 113.8341 | 124.3624 | 143.2598 | 168.6401 | 195.2937 | 228.6298 | 257.9224 | 284.3764 | 311.2991 | 336.3787 | 361.2122
Commercial Biomass | 13.3797 | 14.8309 | 16.282 | 17.7332 | 20.962 | 22.9203 | 33.9514 | 43.8312 | 54.6427 | 65.4709 | 75.3689 | 84.9915 | 94.3088
Nuclear | 7.246 | 8.1522 | 9.0584 | 9.9646 | 9.9226 | 10.8957 | 12.7667 | 14.6897 | 17.1774 | 20.1724 | 23.8595 | 27.6416 | 31.4095
Non-Biomass Renewables | 7.8662 | 8.9642 | 10.0621 | 11.16 | 13.9867 | 16.9541 | 20.2575 | 23.0763 | 26.3875 | 30.2539 | 33.577 | 37.1656 | 41.1038
Energy Reduction

## Slide 44: Primary Energy: 50% reduction
Full Technology Portfolio
No Nuclear and CCS
No Bio CCS
Chart: 
| 1990 | 1995 | 2000 | 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Oil | 136.5998 | 147.8861 | 159.1724 | 170.4588 | 176.0788 | 185.4799 | 184.4971 | 181.1828 | 178.9079 | 177.7472 | 178.9437 | 181.8681 | 186.3747
Natural Gas | 70.3394 | 79.8275 | 89.3156 | 98.8037 | 113.8448 | 127.4344 | 147.2497 | 172.5287 | 195.3516 | 214.9606 | 232.8845 | 247.7666 | 260.7587
Coal | 92.7774 | 103.3057 | 113.8341 | 124.3624 | 143.2598 | 168.6401 | 195.2937 | 228.6298 | 257.9224 | 284.3764 | 311.2991 | 336.3787 | 361.2122
Commercial Biomass | 13.3797 | 14.8309 | 16.282 | 17.7332 | 20.962 | 22.9203 | 33.9514 | 43.8312 | 54.6427 | 65.4709 | 75.3689 | 84.9915 | 94.3088
Nuclear | 7.246 | 8.1522 | 9.0584 | 9.9646 | 9.9226 | 10.8957 | 12.7667 | 14.6897 | 17.1774 | 20.1724 | 23.8595 | 27.6416 | 31.4095
Non-Biomass Renewables | 7.8662 | 8.9642 | 10.0621 | 11.16 | 13.9867 | 16.9541 | 20.2575 | 23.0763 | 26.3875 | 30.2539 | 33.577 | 37.1656 | 41.1038
Energy Reduction

## Slide 45: Electricity production: Reference Scenario
Full Technology Portfolio
No Nuclear and CCS
No Bio CCS
Chart: 
| 1990 | 1995 | 2000 | 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Oil: w/o CCS | 1.3017 | 1.2296 | 1.1575 | 1.0855 | 0.95065 | 0.70638 | 0.44552 | 0.46965 | 0.47381 | 0.46898 | 0.4881 | 0.49436 | 0.50663
Oil: w/ CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Natural Gas: w/o CCS | 1.5555 | 2.1924 | 2.8292 | 3.4661 | 4.5515 | 6.2978 | 7.3625 | 8.4011 | 9.4324 | 10.3888 | 11.4314 | 12.4106 | 13.388
Natural Gas: w/ CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Coal: w/o CCS | 4.3638 | 5.3199 | 6.276 | 7.232 | 8.5915 | 10.7081 | 12.0764 | 13.5475 | 14.8927 | 16.1038 | 17.4422 | 18.719 | 20.0523
Coal: w/ CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Commercial Biomass | 0.052208 | 0.082011 | 0.11181 | 0.14162 | 0.21258 | 0.29571 | 0.3976 | 0.54479 | 0.72861 | 0.93705 | 1.1844 | 1.4537 | 1.7408
Biomass: w/ CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Nuclear | 2.0128 | 2.2645 | 2.5162 | 2.768 | 2.7563 | 3.0266 | 3.5463 | 4.0805 | 4.7715 | 5.6034 | 6.6276 | 7.6782 | 8.7249
Non-Biomass Renewables | 2.1851 | 2.49 | 2.795 | 3.1 | 3.8852 | 4.7095 | 5.6271 | 6.4101 | 7.3299 | 8.4039 | 9.327 | 10.3238 | 11.4177
Electricity Use Reduction

## Slide 46: Electricity production: 2010 Emissions
Full Technology Portfolio
No Nuclear and CCS
No Bio CCS
Chart: 
| 1990 | 1995 | 2000 | 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Oil: w/o CCS | 1.3017 | 1.2296 | 1.1575 | 1.0855 | 0.95065 | 0.70638 | 0.44552 | 0.46965 | 0.47381 | 0.46898 | 0.4881 | 0.49436 | 0.50663
Oil: w/ CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Natural Gas: w/o CCS | 1.5555 | 2.1924 | 2.8292 | 3.4661 | 4.5515 | 6.2978 | 7.3625 | 8.4011 | 9.4324 | 10.3888 | 11.4314 | 12.4106 | 13.388
Natural Gas: w/ CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Coal: w/o CCS | 4.3638 | 5.3199 | 6.276 | 7.232 | 8.5915 | 10.7081 | 12.0764 | 13.5475 | 14.8927 | 16.1038 | 17.4422 | 18.719 | 20.0523
Coal: w/ CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Commercial Biomass | 0.052208 | 0.082011 | 0.11181 | 0.14162 | 0.21258 | 0.29571 | 0.3976 | 0.54479 | 0.72861 | 0.93705 | 1.1844 | 1.4537 | 1.7408
Biomass: w/ CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Nuclear | 2.0128 | 2.2645 | 2.5162 | 2.768 | 2.7563 | 3.0266 | 3.5463 | 4.0805 | 4.7715 | 5.6034 | 6.6276 | 7.6782 | 8.7249
Non-Biomass Renewables | 2.1851 | 2.49 | 2.795 | 3.1 | 3.8852 | 4.7095 | 5.6271 | 6.4101 | 7.3299 | 8.4039 | 9.327 | 10.3238 | 11.4177
Electricity Use Reduction

## Slide 47: Electricity production: 25% reduction
Full Technology Portfolio
No Nuclear and CCS
No Bio CCS
Chart: 
| 1990 | 1995 | 2000 | 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Oil: w/o CCS | 1.3017 | 1.2296 | 1.1575 | 1.0855 | 0.95065 | 0.70638 | 0.44552 | 0.46965 | 0.47381 | 0.46898 | 0.4881 | 0.49436 | 0.50663
Oil: w/ CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Natural Gas: w/o CCS | 1.5555 | 2.1924 | 2.8292 | 3.4661 | 4.5515 | 6.2978 | 7.3625 | 8.4011 | 9.4324 | 10.3888 | 11.4314 | 12.4106 | 13.388
Natural Gas: w/ CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Coal: w/o CCS | 4.3638 | 5.3199 | 6.276 | 7.232 | 8.5915 | 10.7081 | 12.0764 | 13.5475 | 14.8927 | 16.1038 | 17.4422 | 18.719 | 20.0523
Coal: w/ CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Commercial Biomass | 0.052208 | 0.082011 | 0.11181 | 0.14162 | 0.21258 | 0.29571 | 0.3976 | 0.54479 | 0.72861 | 0.93705 | 1.1844 | 1.4537 | 1.7408
Biomass: w/ CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Nuclear | 2.0128 | 2.2645 | 2.5162 | 2.768 | 2.7563 | 3.0266 | 3.5463 | 4.0805 | 4.7715 | 5.6034 | 6.6276 | 7.6782 | 8.7249
Non-Biomass Renewables | 2.1851 | 2.49 | 2.795 | 3.1 | 3.8852 | 4.7095 | 5.6271 | 6.4101 | 7.3299 | 8.4039 | 9.327 | 10.3238 | 11.4177
Electricity Use Reduction

## Slide 48
Full Technology Portfolio
No Nuclear and CCS
No Bio CCS
Chart: 
| 1990 | 1995 | 2000 | 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Oil: w/o CCS | 1.3017 | 1.2296 | 1.1575 | 1.0855 | 0.95065 | 0.70638 | 0.44552 | 0.46965 | 0.47381 | 0.46898 | 0.4881 | 0.49436 | 0.50663
Oil: w/ CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Natural Gas: w/o CCS | 1.5555 | 2.1924 | 2.8292 | 3.4661 | 4.5515 | 6.2978 | 7.3625 | 8.4011 | 9.4324 | 10.3888 | 11.4314 | 12.4106 | 13.388
Natural Gas: w/ CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Coal: w/o CCS | 4.3638 | 5.3199 | 6.276 | 7.232 | 8.5915 | 10.7081 | 12.0764 | 13.5475 | 14.8927 | 16.1038 | 17.4422 | 18.719 | 20.0523
Coal: w/ CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Commercial Biomass | 0.052208 | 0.082011 | 0.11181 | 0.14162 | 0.21258 | 0.29571 | 0.3976 | 0.54479 | 0.72861 | 0.93705 | 1.1844 | 1.4537 | 1.7408
Biomass: w/ CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Nuclear | 2.0128 | 2.2645 | 2.5162 | 2.768 | 2.7563 | 3.0266 | 3.5463 | 4.0805 | 4.7715 | 5.6034 | 6.6276 | 7.6782 | 8.7249
Non-Biomass Renewables | 2.1851 | 2.49 | 2.795 | 3.1 | 3.8852 | 4.7095 | 5.6271 | 6.4101 | 7.3299 | 8.4039 | 9.327 | 10.3238 | 11.4177
Electricity Use Reduction
Electricity production: 50% reduction

## Slide 49: Onshore wind energy capacity in the 50% Scenarios
About 837 GWe installed capacity in 2022 (actual)
2000 GWe installed capacity by 2030
Almost 9000 GWe installed capacity by 2050
Note: Assumes a 25% average future global onshore wind capacity factor
Much more to get to net-zero
Almost 3700 GWe installed capacity by 2050

## Slide 50: Number of wind turbines in 50% reduction scenarios
330,000 additional 5 MW turbines from 2017 through 2030
Around 1.4 million additional 5 MW turbines from 2030 through 2050
341k turbines in 2017 (actual)
600,000 additional 5 MW turbines from 2017 through 2050
Note: Assumes a 25% average future global onshore wind capacity factor
Many more to get to net-zero

## Slide 51
What is the role of institutions in such transitions?

## Slide 52: Many non-economic factors could affect the rate at which technologies deploy
Institutions
Policy/regulatory uncertainty
Public perceptions

## Slide 53: Institutional capacities are non-uniform across the globe
Source: World Economic Forum Global Competitiveness Survey

## Slide 54: Institutional factors can affect investors’ perceptions of risks
AFRICAN WIND FARM
Cost of debt ~ 12-13%
U.S. WIND FARM
Cost of debt ~ 8-9%

## Slide 55: Implications of nonuniform investment risks
Nonuniform investment risks can have important implications as investors respond to risks by
  Expecting higher returns for riskier projects
  Delaying or forgoing investments
  Preferring to invest in existing, familiar technologies
How could heterogeneity in investment risks influence cost and distribution of climate change mitigation?

## Slide 56: Incorporating risk perceptions in GCAM resulted in three effects
Reduced investments in high risk low-carbon technologies (e.g. nuclear) and increased investments in BECCS and energy efficiency
Shift of investments from developing to developed world
Higher costs for meeting a given emissions goal
  About 40% higher carbon price for a 50% reduction in CO2 emissions by 2050
Investments in electricity for 50% reduction in CO2 emissions by 2050
(Billion 2012 USD per year)
Changes relative to uniform investment risks

## Slide 57: Key Insights from the study
Major efforts to improve the institutional environment need to be essential elements of a larger strategy for reducing emissions cost-effectively
It is plausible that institutional reforms may even be more important than technology-focused policies.
Absent such reforms, mitigation effort could be disproportionately focused on countries where investment risks are lower.

## Slide 58: Some emerging areas of energy systems research in IAMs
Stranded assets under climate mitigation
Effect of trade and geopolitical relationships on energy system transitions
Linkages with mineral supply chains: Implications of mineral supply chains for energy system transitions and vice versa
Linkages with sustainable development goals
Spatial and sub-annual details to better capture intra-annual dynamics (e.g. storage in the power sector)
  Impacts of changing intra-annual load patterns driven by climate, electric vehicle charging, etc.
Impacts of behavioral changes

## Slide 59: Questions

## Slide 60: The timing of net-zero varies by sector
Boxes indicate 25th and 75th percentiles, center black line is the median, while whiskers indicate 1.5x the inter-quartile range. The vertical dashed lines represent the median point at which emissions in the scenarios have dropped by 95% (pink) and 97.5% (purple), respectively. Dots represent individual scenarios. The fraction indicates the number of scenarios reaching net-zero by 2100 out of the total sample. Source: AR6 Scenario Database.
Black vertical line is the median across many IAM scenarios
Note that the range across scenarios is quite wide
Source: IPCC, AR6

## Slide 61: Mitigation scenarios are characterized by a major upscaling of low- and zero- carbon energy
Total Low-Carbon Energy Supply
No Policy Scenarios that are consistent with >4°C warming by the end of the century
Scenarios that are consistent with 3°C warming by the end of the century
Scenarios that are consistent with 2°C warming by the end of the century
Source: IPCC, AR5

## Slide 62: Mitigation scenarios consistent with 2°C warming are characterized by a tripling to nearly a quadrupling of the share of zero- and low-carbon energy supply
2010
Source: IPCC, AR5
Scenarios that are consistent with 2°C warming by the end of the century