## Slide 1: IAM in National Decarbonization Pathways
PLCY-798K
Integrated Human-Earth System Modeling and Policy Assessment
April 1, 2023

## Slide 2: Key questions being asked in national contexts
Research/policy questions
  Deep decarbonization pathways
  Sectoral specific transitions to a low-carbon energy system
  Impacts of specific policies
  Societal implications
    Air quality/health
    Employment, just transition
    Economic growth, etc.
  Climate change impacts
Stakeholders
  Governments: policy and science offices
  Business
  NGOs
  How to inform decision making
Tools: different tools / combinations of tools can be applied depending on research question

## Slide 3
The U.S. Long-Term Strategy

## Slide 4: Global Change Analysis Model
Model Coverage
384 Land Regions
32 Energy & Economy Regions
235 Water Basins
GCAM is a global hierarchical equilibrium integrated assessment model
GCAM links Economic, Energy, Land-use, Water, and Climate systems in a technology-rich model
Runs to 2100 in 5-year time-steps
Emissions of 16 greenhouse gases (GHG) and air pollutants are tracked
GCAM is natively coupled to a simple climate model HECTOR, but can also be coupled to Energy Exascale Earth System Model (E3SM)
GCAM is a community model, download link and documentation available at: http://jgcri.github.io/gcam-doc/toc.html
GCAM is primarily developed with support from Office of Science, but has wide reaching applications in policy, science, and philanthropies
4

## Slide 5: Global Change Analysis Model
Image source: Hejazi, M. et al. Long-term global water projections using six socioeconomic scenarios in an integrated assessment modeling framework. Technol. Forecast. Soc. Change 81, 205–226 (2014).

## Slide 6: GHG Emissions
Low CDR Med CDR High CDR
+ High Energy Demand

## Slide 7
Standard Elec Advanced Elec
Electricity Generation

## Slide 8
Power Sector Transition

## Slide 9: Refined Liquids Production
Low CDR Med CDR High CDR
+ High Energy Demand

## Slide 10: Building Final Energy
Reference Buildings Advanced Buildings

## Slide 11: Industry Final Energy
Standard Industry Advanced Industry

## Slide 12: Transport Final Energy
Standard Transport Advanced Transport

## Slide 13: Passenger LDV Sales
Standard Transport Advanced Transport

## Slide 14: Passenger LDV Service Output
Standard Transport Advanced Transport

## Slide 15: Freight Truck Sales
Standard Transport Advanced Transport

## Slide 16: Freight Road Service Output
Standard Transport Advanced Transport

## Slide 17
The U.S. Long-Term Strategy

## Slide 18: Lessons Learned from the U.S. LTS
Net-Zero emission modeling is really hard
Net-Zero GHG modeling is really REALLY hard
Negative part is just as important as the positive part
We can’t just wave a magic wand (carbon tax) and call it done
We need to listen to the detailed sector models and experts
Getting to net-zero emission is really hard

## Slide 19
The 2015 Paris Agreement set up a process to revise countries’ emission reduction pledges every five years
The United Nations’ 26th Conference of Parties (COP) held in Glasgow in November 2021 was a waypoint in the updating process

## Slide 20
Over 150 countries submitted updated or new Nationally Determined Contributions (NDCs) outlining actions through 2030
Source: https://www.climatewatchdata.org/

## Slide 21
Countries also submitted long-term strategies and net-zero pledges outlining actions through mid-century
Source: https://www.climatewatchdata.org/

## Slide 22: U.S. Long-Term Strategy for Net-Zero Pathways
Notes: Miralles-Wilhelm, F., Hejazi, M., Kim, S., Yonkofski, C., Watson, D., Kyle, P., ... & Clarke, L. (2018). Water for Food and Energy Security: An Assessment of the Impacts of Water Scarcity on Agricultural Production and Electricity Generation in the Middle East and North Africa. World Bank.
Jeon, S., Roh, M., Oh, J., & Kim, S. (2020). Development of an Integrated Assessment Model at Provincial Level: GCAM-Korea. Energies, 13(10), 2565.
Binsted, M., Iyer, G., Patel, P., Graham, N., Ou, Y., Khan, Z., ... & Wise, M. (2021). GCAM-USA v5. 3_water_dispatch: Integrated modeling of subnational US energy, water, and land systems within a global framework. Geoscientific Model Development Discussions, 1-39.
Yu, S., Horing, J., Liu, Q., Dahowski, R., Davidson, C., Edmonds, J., ... & Clarke, L. (2019). CCUS in China’s mitigation strategy: insights from integrated assessment modeling. International Journal of Greenhouse Gas Control, 84, 204-218.
Khan, Z., Wild, T. B., Carrazzone, M. E. S., Gaudioso, R., Mascari, M. P., Bianchi, F., ... & Castillo, R. M. (2020). Integrated energy-water-land nexus planning to guide national policy: an example from Uruguay. Environmental Research Letters, 15(9), 094014.
Wild, T. B., Khan, Z., Zhao, M., Suriano, M., Bereslawski, J. L., Roberts, P., ... & Ojeda‐Matos, G. (2021a). The Implications of Global Change for the Co‐Evolution of Argentina's Integrated Energy‐Water‐Land Systems. Earth's Future, 9(8), e2020EF001970.
Wild, T. B., Khan, Z., Clarke, L., Hejazi, M., Bereslawski, J. L., Suriano, M., ... & Birnbaum, A. (2021b). Integrated energy-water-land nexus planning in the Colorado River Basin (Argentina). Regional Environmental Change, 21(3), 1-16.
Yu, S., Evans, M., Kyle, P., Vu, L., Tan, Q., Gupta, A., & Patel, P. (2018). Implementing nationally determined contributions: building energy policies in India’s mitigation strategy. Environmental Research Letters, 13(3), 034034.
Arbuckle, E. J., Binsted, M., Davies, E. G., Chiappori, D. V., Bergero, C., Siddiqui, M. S., ... & Macaluso, N. (2021). Insights for Canadian electricity generation planning from an integrated assessment model: Should we be more cautious about hydropower cost overruns?. Energy Policy, 150, 112138.
Calvin, K., Patel, P., Clarke, L., Asrar, G., Bond-Lamberty, B., Cui, R. Y., ... & Wise, M. (2019). GCAM v5. 1: representing the linkages between energy, water, land, climate, and economic systems. Geoscientific Model Development, 12(2), 677-698.

## Slide 24: Scenarios

## Slide 25: Electricity Generation

## Slide 26: CO2 Emissions

## Slide 28
The dramatic GHG reduction demonstrates the need for rapid changes in entire energy system.
Negative emission technologies are critical to offset hard-to-abate emissions .
Mt CO2e
Year
Chart: NZ2050
| 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Electricity | 177.9623 | 251.4377 | 267.8605 | 265.6469 | 240.8944 | 160.1147 | 90.7489 | 31.02 | -15.172 | -36.105
Industry | 202.3089 | 223.9899 | 282.2089 | 293.5144 | 228.951 | 204.4645 | 173.8518 | 134.6743 | 85.7422 | 48.541
Transportation | 85.1909 | 89.597 | 101.8441 | 105.894 | 91.0223 | 81.0418 | 64.0867 | 49.9666 | 37.3014 | 24.8276
Building | 61.8857 | 55.0276 | 59.4692 | 61.617 | 56.4654 | 53.2147 | 46.0234 | 37.3166 | 28.0323 | 23.1026
Agriculture | 21.8959 | 21.9432 | 23.035 | 23.0791 | 17.9524 | 17.9276 | 16.9226 | 16.3109 | 15.5535 | 14.8386
DAC | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | -1.325e-07 | -43.8728
LULUCF | -47 | -46 | -45 | -45 | -44.875 | -43.0625 | -39.4375 | -37.625 | -35.8125 | -34
Chart: NZ2050_Nuc
| 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Electricity | 177.962 | 251.438 | 267.86 | 265.647 | 240.429 | 160.898 | 91.519 | 34.312 | -6.5 | -24.848
Industry | 202.309 | 223.99 | 282.223 | 293.528 | 234.397 | 204.566 | 174.548 | 133.192 | 78.56 | 24.943
Transportation | 85.191 | 89.597 | 101.844 | 105.894 | 96.061 | 81.225 | 64.46 | 50.298 | 37.541 | 24.73
Building | 61.886 | 55.028 | 59.469 | 61.617 | 56.326 | 52.038 | 44.531 | 36.374 | 27.685 | 21.53
Agriculture | 21.896 | 21.943 | 23.035 | 23.079 | 18.973 | 17.987 | 17.049 | 16.389 | 15.616 | 14.853
DAC | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | -27.255
LULUCF | -47 | -46 | -45 | -45 | -44.875 | -43.063 | -39.438 | -37.625 | -35.813 | -34
Chart: Curpol
| 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Electricity | 177.962 | 251.438 | 267.86 | 265.647 | 241.7945 | 209.2353 | 174.7756 | 121.557 | 108.8479 | 109.7961
Industry | 202.309 | 223.99 | 282.223 | 293.528 | 311.6186 | 317.3222 | 318.8494 | 321.7602 | 321.2269 | 309.411
Transportation | 85.191 | 89.597 | 101.844 | 105.894 | 102.8711 | 93.7494 | 83.2684 | 74.6701 | 67.0093 | 59.206
Building | 61.886 | 55.028 | 59.469 | 61.617 | 60.7394 | 59.6273 | 55.3837 | 51.4414 | 47.4486 | 41.7894
Agriculture | 21.896 | 21.943 | 23.035 | 23.079 | 22.5968 | 22.1229 | 21.4144 | 21.1305 | 20.6039 | 19.8047
DAC | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
LULUCF | -47 | -46 | -45 | -45 | -44.875 | -43.0625 | -39.4375 | -37.625 | -35.8125 | -34
Result
GHG Emission by Sector
Chart: NZ2050_NoCCS
| 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Electricity | 177.962 | 251.438 | 267.86 | 265.647 | 243.1452 | 165.4041 | 107.7688 | 69.1787 | 28.861 | 0
Industry | 202.309 | 223.99 | 282.223 | 293.528 | 234.7483 | 207.8297 | 173.8969 | 127.1048 | 74.7572 | 4.5741
Transportation | 85.191 | 89.597 | 101.844 | 105.894 | 95.8387 | 80.6078 | 63.0436 | 47.5867 | 32.5638 | 7.245
Building | 61.886 | 55.028 | 59.469 | 61.617 | 56.1876 | 51.8275 | 42.9083 | 31.6107 | 20.6241 | 8.25
Agriculture | 21.896 | 21.943 | 23.035 | 23.079 | 18.8982 | 17.8622 | 16.7184 | 16.1885 | 15.3547 | 14.7141
DAC | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
LULUCF | -47 | -46 | -45 | -45 | -44.875 | -43.0625 | -39.4375 | -37.625 | -35.8125 | -34
Hanwoong KIM Center for Sustainable Development 15th IAMC, November 30, 2022
Notes: Along with the GHG emission pathways, the GHG emissions were classified by sector to find out the reduction burden of each sector.
Compared to Curpol on the left, the other three scenarios show a rapid reduction in GHG emissions, which requires significant changes in the energy system.
In addition, negative emissions technology seems essential to address the remaining GHG in 2050 in common across scenarios.
Our study shows that the power and industrial sectors are the most significant contributors to carbon neutrality, followed by transportation and buildings.

## Slide 29
Carbon-neutrality require drastic change: Substituting fossil fuels to low carbon sources
TWh
Chart: CurPol
| 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Oil | 21.0416 | 14.963 | 12.8481 | 11.2585 | 10.1854 | 8.6418 | 7.0811 | 5.6042 | 4.1295 | 2.7264
Gas | 59.1847 | 101.5208 | 116.4981 | 149.2364 | 185.083 | 211.9779 | 237.1746 | 248.0545 | 235.4809 | 222.1167
Gas CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
CHP | 22.8798 | 25.1814 | 8.1462 | 5.9266 | 7.6012 | 7.917 | 8.213 | 8.7036 | 8.9199 | 8.3834
Coal | 134.0758 | 200.4906 | 210.2681 | 195.7225 | 162.1658 | 119.9378 | 77.6322 | 15.4931 | 4.249 | 0
Coal CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Nuclear | 146.7831 | 148.5958 | 163.2012 | 158.8656 | 149.4711 | 136.6153 | 120.4778 | 102.2808 | 84.0839 | 67.9467
Biomass | 0.045001 | 0.346 | 3.13 | 8.1054 | 10.4452 | 12.7667 | 14.0981 | 22.32 | 28.251 | 40.4388
Biomass CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Geothermal | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Hydro | 3.673 | 3.879 | 4.2076 | 4.7331 | 5.2586 | 5.7842 | 6.3098 | 7.1887 | 8.0676 | 8.9465
Hydrogen | 0 | 0 | 0 | 2.6221 | 7.1091 | 10.6189 | 13.9413 | 18.7609 | 23.9145 | 26.5231
Chart: NZ2050
| 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Oil | 21.0416 | 14.963 | 12.848 | 11.2328 | 9.5246 | 7.2812 | 4.8216 | 2.2837 | 0.55804 | 0.11728
Oil CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gas | 59.1847 | 101.5208 | 116.539 | 149.1756 | 219.5498 | 230.7109 | 230.4964 | 168.2835 | 76.5917 | 22.4875
Gas CCS | 0 | 0 | 0 | 0 | 0 | 8.2748 | 22.6773 | 51.1156 | 84.2794 | 103.7411
CHP | 22.8798 | 25.1814 | 8.1454 | 5.8515 | 8.4139 | 8.5756 | 7.4718 | 5.4603 | 3.0368 | 1.7103
Coal | 134.0758 | 200.4906 | 210.2864 | 195.8847 | 159.3547 | 93.9417 | 30.6436 | 1.9356 | 0.061874 | 0
Coal CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Nuclear | 146.7831 | 148.5958 | 163.2208 | 158.8614 | 149.4669 | 136.6111 | 120.4736 | 102.2767 | 84.0797 | 67.9425
Biomass | 0.045001 | 0.346 | 3.1314 | 8.124 | 11.9628 | 12.8945 | 10.0697 | 5.4171 | 0.9685 | 0.1785
Biomass CCS | 0 | 0 | 0 | 0 | 1.1457 | 3.5307 | 8.596 | 23.6969 | 47.9076 | 68.8617
Geothermal | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Hydro | 3.673 | 3.879 | 4.2076 | 4.7331 | 5.2586 | 5.7842 | 6.3098 | 7.1887 | 8.0676 | 8.9465
Chart: NZ2050_Nur
| 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Oil | 21.0416 | 14.963 | 12.848 | 11.2328 | 9.4606 | 6.6252 | 4.1629 | 2.0353 | 0.50129 | 0.073363
Oil CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gas | 59.1847 | 101.5208 | 116.539 | 149.1756 | 188.3427 | 189.6045 | 182.5665 | 127.4126 | 54.8164 | 10.3365
Gas CCS | 0 | 0 | 0 | 0 | 0 | 3.5629 | 8.6861 | 18.5261 | 31.0889 | 38.9611
CHP | 22.8798 | 25.1814 | 8.1454 | 5.8515 | 7.9387 | 7.2485 | 6.3996 | 5.132 | 3.0062 | 1.4111
Coal | 134.0758 | 200.4906 | 210.2864 | 195.8847 | 160.8097 | 101.9261 | 38.4122 | 2.8023 | 0.080654 | 0
Coal CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Nuclear | 146.7831 | 148.5958 | 163.2208 | 158.8614 | 196.5714 | 257.695 | 311.7792 | 377.5144 | 447.2953 | 491.53
Biomass | 0.045001 | 0.346 | 3.1314 | 8.124 | 10.8256 | 11.6744 | 9.8431 | 7.0392 | 1.5845 | 0.14942
Biomass CCS | 0 | 0 | 0 | 0 | 0.64929 | 1.7172 | 3.4964 | 10.2253 | 25.1056 | 38.661
Geothermal | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Hydro | 3.673 | 3.879 | 4.2076 | 4.7331 | 5.2586 | 5.7842 | 6.3098 | 7.1887 | 8.0676 | 8.9465
Year
Result
Electricity generation
Chart: NZ2050_NoCCS
| 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Oil | 21.0416 | 14.963 | 12.6678 | 11.2301 | 9.1105 | 6.4292 | 3.3401 | 0.86684 | 0.10452 | 0.00048558
Oil CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gas | 59.1847 | 101.5208 | 122.2867 | 150.6782 | 216.7688 | 242.958 | 239.1037 | 140.2712 | 30.9596 | 1.8196
Gas CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
CHP | 22.8798 | 25.1814 | 9.3604 | 11.4686 | 13.1884 | 11.4325 | 8.204 | 4.4413 | 1.9337 | 0.16289
Coal | 134.0758 | 200.4906 | 213.1044 | 197.3744 | 151.7311 | 64.7642 | 9.6165 | 0.24316 | 0.0037303 | 0
Coal CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Nuclear | 146.7831 | 148.5958 | 166.2267 | 161.7758 | 152.3814 | 139.5256 | 123.3881 | 105.1911 | 86.9942 | 70.8567
Biomass | 0.045001 | 0.346 | 2.3915 | 7.6914 | 12.8619 | 17.4722 | 19.7738 | 26.0154 | 20.4439 | 3.0596
Biomass CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Geothermal | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Hydro | 3.673 | 3.879 | 4.2076 | 4.7331 | 5.2586 | 5.7842 | 6.3098 | 7.1887 | 8.0676 | 8.9465
Hanwoong KIM Center for Sustainable Development 15th IAMC, November 30, 2022
Notes: Compare to current policy scenario, a much faster transition occurs when climate policies are in place.
The three carbon-neutral scenarios in common suggest coal phase-out under the three carbon neutrality pathways.
However, each NZ scenario provides different technology options.
A. The NZ2050 scenario is made up of CCS technology and renewable energy.
B. In the NZ2050_Nuc scenario, centered on nuclear power.
Due to limited CCS technology, C. NZ2050_NoCCS scenario relies more on renewable energy than NZ2050.

## Slide 30
[Source: KIER, Renewable Energy Potential Map, 2022]
Result
Potential resources & land requirement
Electricity Generation (GWh/y)
Capacity (GW)
Primary Energy (toe/y)
Solar
75.57%
Solar
83.69%
Solar
75.57%
On_Wind
24.43%
On_Wind
24.43%
On_Wind
16.31%
Solar
On_Wind
Natural Resources Potential (GWh/y)
Solar power plants_NZ2050_NoCCS
Nuclear power plants_NZ2050_Nuc
1GW nuclear power plant requires the land size of 0.745km2 (including the geological land and sea area)
X 6
605.2KM2
10% of the size of Seoul
[Source: Korea energy agency, Renewable Energy White Paper, 2020]
[Source: KOPIA, A plan to secure locations for each photovoltaic area to achieve carbon]
[Source: National Assembly Budget Office "Report on Area Required by Power Generation Source" 2017]
GCAM_NZ2050_NoCCS
Hanwoong KIM Center for Sustainable Development 15th IAMC, November 30, 2022
Notes: The left figure shows Korea's renewable energy technical potential.
In Korea, Solar power has about 1000 GW of technical potential.
The most extreme scenario, the NZ2050_NoCCS scenario, requires about 6 times the size of Seoul.
However, in the NZ2050_nuc scenario, 2 times the size of Seoul for solar power
and only about 10% of the area of Seoul is needed to build a nuclear power plant.
If Korea's energy policy focuses only on solar technology, the feasibility of achieving 2050 carbon neutrality may be lowered due to land use problems.

## Slide 31
With Storage
Without Storage
GHG emissions pathways and Electricity Generation by technology
Electricity Capacity by technology
Mt CO2eq
TWh
GW
Offshore_wind
Onshore_wind
Solar_PV
Other Renewable Energy
Hydrogen
LNG
Coal
Nuclear
GHG Emission
NZ2050 Total Electricity Generation
Offshore_wind
Onshore_wind
Solar_PV
Other Renewable Energy
Hydrogen
LNG
Coal
Nuclear
Renewable Energy Potential
Solar: 370, 300 (NZ2050)
Wind: 200, 110 (NZ2050)
Summer and winter power generation (Storage option)
Hanwoong KIM Center for Sustainable Development 15th IAMC, November 30, 2022
Notes: To concern of power system stability when we reach to 2050 Net zero, I compare with the recent Korea's report, which is considering more deeply on transmission constructing and 8760 hours resolution for electricity generation. This assessment and this study are largely consistent in terms of generation, capacity by technology.

## Slide 32
USA – 50-52% net GHG emission reduction below 2005 levels
USA
EU
China
India
Brazil
Rest of the world
PNNL BAU
Mitigation due to current policy
Mitigation for NDC and net-zero pledge
2015 NDC
2021 NDC 50%
2021 NDC 52%
In the absence of additional climate policy, U.S. GHG emissions are projected to increase again.
U.S. updated NDC target is to reduce its GHG emissions 50-52% below 2005 levels by 2030.
U.S. current policies contribute to emission reductions in 2030
GHG emissions (Gt CO2e including land use)

## Slide 33
EU – 55% emission reduction below 1990 levels
USA
EU
China
India
Brazil
Rest of the world
PNNL BAU
Mitigation due to current policy
2015 NDC
2021 NDC
GHG emissions (Gt CO2e including land use)
In the absence of climate policy, EU’s GHG emissions are projected to slowly increase again.
EU current policy emissions can overachieve its 2015 NDC (40% below 1990).
Meeting the updated 55% target requires additional GHG emissions reduction.
Mitigation for NDC and net-zero pledge

## Slide 34
China – 2030 peak; 60-65% CO2/GDP reduction from 2005
USA
EU
China
India
Brazil
Rest of the world
PNNL BAU
Mitigation due to current policy
Mitigation for 2060 carbon-neutrality goal
60% CO2 / GDP reduction
CO2 emissions (Gt CO2e excluding land use)
China’s CO2 emission is projected to peak on its own in the absence of climate policy.
China’s NDC target: Peak CO2 emissions by 2030 at the latest; Lower CO2 emissions per unit of GDP by 60% to 65% from 2005 levels
PNNL projects emissions between 60-65% CO2 intensity reduction range.
China also pledges a carbon-neutrality goal by 2060, leading to large emission reductions after peaking in 2030.
65% CO2 / GDP reduction

## Slide 35
India – 33-35% emissions/GDP reduction from 2005
USA
EU
China
India
Brazil
Rest of the world
Mitigation due to current policy
Mitigation for NDC
GHG emissions (Gt CO2e excluding land use)
In the absence of climate policy, India’s GHG emissions are projected to increase over time, consistent with historical rate.
India’s NDC includes:
  to reduce the emissions intensity of its GDP by 33-35%;
  to achieve 40% electric power installed capacity from non-fossil fuels
  to create an additional carbon sink of 2.5-5 billion tCO2e
PNNL projects lower emissions in 2030 because of lower reference scenario, which reflects updated assumptions in renewable cost and new technologies.
Climate Action Tracker assessment

## Slide 36
We compiled 100+ NDCs, long-term strategies, and net-zero pledges for modeling in GCAM
USA
EU

## Slide 37
Historical
Projected
USA
EU
Other developed countries
China
India
Rest of the world
Other developed countries:
Canada, Japan, Australia, New Zealand
Global GHG emissions: Reference No New Policy

## Slide 38
Historical
Projected
Other developed countries:
Canada, Japan, Australia, New Zealand
USA
EU
China
India
Rest of the world
Global GHG emissions: Updated Pledges Continued Ambition

## Slide 39
Global GHG: remaining emissions
Historical
Projected
Other developed countries:
Canada, Japan, Australia, New Zealand
USA
EU
China
India
Rest of the world
Emissions mitigation

## Slide 40
Historical
Projected
Other developed countries:
Canada, Japan, Australia, New Zealand
USA
EU
China
India
Rest of the world
Emissions mitigation
Increased mitigation
Global GHG emissions: Updated Pledges Increased Ambition

## Slide 41
* Co-lead author
*

## Slide 42: Using GCAM, we constructed emissions pathways. Using a simple climate model (MAGICC) in a probabilistic setup, we evaluated temperature distributions in 2100

## Slide 43: Temperature distributions after accounting for pledges submitted during and after COP-21 are improved

## Slide 44: Key Takeaways
Collectively, the updated and new 2021 climate pledges are stronger than the 2015 pledges
There’s more than 50% chance that the temperature will remain below 2 degrees if these pledges are implemented as stated
If combined with increased ambition, the probability under 2 degrees can be increased to close to 70%
However, the pledges still fall far short of achieving 1.5 degrees with a reasonable chance

## Slide 45: Paris to Glasgow: Improved Pledges vs. Improved Models
USA
We conducted additional simulations combine the emissions scenarios in this study (based on GCAM 5.3) and those from Fawcett et al. 2015 (based on GCAM 4.0) with the versions of MAGICC used in the two studies (MAGICC6 and MAGICC7).
The additional simulations suggest that most of the differences in probabilistic temperature outcomes below 2°C between Fawcett et al. 2015 and this study can be attributed to the updated emissions trajectories, which are in turn driven by the updated pledges, LTSs, net-zero pledges, and other recent societal, policy, and technological trends.
< 1.5 °C
< 2.0 °C
> 4.0 °C

## Slide 46: Broad context – increasing details in IAM
Regional
Temporal
Sectoral
Flexible Scale
Current examples
GCAM-USA; GCAM-China; GCAM-Canada; GCAM-India; GCAM-SEAsia; GCAM-LAC; City Scale Modeling
Flexible Time Scale
GCAM Core runs at 5 years; capability to run at one year; ancillary models run at finer scale
Notes: Sha

## Slide 47: Strengths and weaknesses of detailed IAMs compared to global IAMs
Strengths:
Capture regional heterogeneity within a country
Analyze subnational policy / action
Explore interactions between states/provinces
More policy relevant
Weaknesses
Data intensive, more difficult to calibrate
Greater memory requirements
Longer runtime
Solution challenges

## Slide 48: Unique features of GCAM-China
Socioeconomics at the provincial level
  Population
  GDP
Energy transformation at the provincial level
  Electricity generation and refining by province
  Electricity trade within 6 grid regions
Renewable and carbon storage at provincial level
  Wind and solar
  Carbon storage
Coal and nuclear power generation at the plant level
Final energy demand at the provincial level
  Buildings: commercial, urban residential, and rural residential
  Transportation: passenger & freight with detailed technologies
  Industry: 9 subsectors

## Slide 49: Policies: Renewable deployment in China
Minimum provincial non-hydro renewable obligation
(% of generation)
Sources: National Energy Administration, June 2020.
https://www.energypolicy.columbia.edu/research/commentary/trends-and-contradictions-china-s-renewable-energy-policy.
NDC: 1200 GW Solar and Wind Capacity by 2030

## Slide 50: Example: Co-benefits of Air Quality and Climate Policies
With the implementation of the Clean Air Action, PM2.5 exposure in China has been decreased by 32% during 2013-2017 (from 67 ug/m3 to 45 ug/m3), leading to a 14% reduction in premature deaths due to long-term exposure (from 1.2 million in 2013 to 1.0 million in 2017).
Pollution reductions during 2013-2017 were mainly benefited from strict end-of-pipe control measures by the implementation of the Action Plan. The roles of energy-climate policy are positive but minor.
What has worked to reduce emissions and mortality in the past may be less effective in the future.

## Slide 51: Example: Model Coupling to Study Health Co-benefits
Source: Liu et al. Under Review

## Slide 52: Example: Model Coupling to Study Health Co-benefits
Source: Liu et al. Under Review

## Slide 53: Example: Finding Feasible Coal Phaseout Pathways
Source: Cui et al. 2021.

## Slide 54: GCAM-USA
GCAM: Global Change Assessment Model
  Integrated Assessment Model of Economic, Energy, Land-use, Water, Emissions and Climate systems
  Modeling of future emissions scenarios to 2100
  Emissions of 16 greenhouse gases and short-lived species
  GCAM is an open-source community model
GCAM-USA is a version of GCAM with state-level detail in the United States.
The 50-state version is embedded within the global version of GCAM.
It is actively being used to explore energy-water-land interactions and conduct policy analysis

## Slide 55: Subnational actors in climate mitigation
Hultman, N.E., Clarke, L., Frisch, C. et al. Fusing subnational with national climate action is central to decarbonization: the case of the United States. Nat Commun 11, 5255 (2020). https://doi.org/10.1038/s41467-020-18903-w. Fig. 1.

## Slide 56: Modeled Scenarios
Existing Policies
Includes current subnational measures (below) and major climate provisions from IIJA and IRA
IIJA investments in transportation infrastructure
IRA investments in clean energy, energy efficiency, methane fee in oil and gas sector.
State and local-level renewable portfolio standards and RE targets, building efficiency targets, transportation sales targets
Projected market forces and other existing policies a cross all sectors (i.e. Corporate Average Fuel Economy standards)
Beyond 50
Layers on federal and non-federal policies across all sectors that achieve the 50-52% reductions needed to meet the NDC
Existing policies
Enhanced fuel efficiency standards
Methane fee across all sectors
Coal phaseout
CCS requirement for new gas
Heightened renewable portfolio standards and RE targets, building efficiency targets, transportation sales targets
Enhanced electrification for buildings and industry sectors through gas bans and buy clean policies

## Slide 57
Emissions reductions under an “all-in” climate pathway to achieve the U.S. climate target by 2030
The existing policies scenario shows a majority of reductions from the energy and transportation sectors, with significant additional reductions from methane, largely driven by IRA, can achieve 39% reductions by 2030 from 2005 levels with potential for 42% reductions with accelerated implementation.
The Beyond 50 scenario incorporates the climate-smart application of IRA from primarily states, with an all-of-society, accelerated approach to a national climate strategy and shows a pathway for the United States to achieve 52% emissions reductions from 2005 levels by 2030.

## Slide 58: Transport sector results
Existing policies achieves significant electrification for passenger cars
IIJA investment in transport infrastructure and bus electrification
IRA EV tax credits
Corporate Average Fuel Economy (CAFE) standards
State-level ZEV sales targets
Beyond 50 strengthens electrification for buses and freight trucks
Heightened state-level ZEV sales targets
100% bus electrification
Vehicle miles traveled reduction policies
Improved CAFE standards

## Slide 59: Transport report shows contribution of federal and non-federal actors to achieve NDC
Transportation emissions need to decrease by 34% to meet the NDC
Current Measures reduce emissions by 350 MtCO₂ (19%)
Remaining 15% must come from non-federal and federal actors
  Non-federal action: 92 MtCO₂ (5%)
  Congressional EV tax credit: 55 MtCO₂ (3%)
  Additional federal actions: 120 MtCO₂ (7%)
97% of reductions occur in light-duty and heavy-duty vehicles
Zhao, A., McJeon, H., Cui, R., Cyrs, T., Feldmann, J., Iyer, G., Kathleen Kennedy, Kevin Kennedy, S. Kennedy, O’Keefe, K., Rajpurohit, S., Rowland, L., & Hultman, N. (2022). An “All-In” pathway to 2030: Transportation sector emissions reduction potential. Center for Global Sustainability, University of Maryland and America Is All In. Available at www.AmericaIsAllIn.com. 8pp.

## Slide 60: Power sector results
Existing policies reaches 71% clean electricity by 2030.
  IRA tax credits for renewables, CCS, hydrogen
  Energy Investment Refinancing program
  State- and city-level renewable energy targets
Beyond 50 reaches 80% clean electricity by 2030
  Coal phaseout
  More ambitious state- and city-level renewable energy targets

## Slide 61: Methane sector results
Existing policies achieves 10% reductions in methane emissions from 2020 levels
IRA oil and gas methane fee
IRA methane-specific agriculture provisions
Beyond 50 achieves over 30% reductions
Methane fee across all sectors
Strengthened EPA regulations on oil and gas methane
State-level standards on existing and new oil and gas sources, emissions standards in the agriculture sector and implementation of agricultural mitigation strategies , waste- reduction policies

## Slide 62
Methane report shows contribution of federal and non-federal actors to achieve NDC
Non-federal action achieves nearly 16% methane emissions reductions below 2020 levels by 2030
With federal action, we can achieve over 30%
Zhao, A., K. O’Keefe, H. McJeon, K. Clark-Sutton, R. Cui, J. Feldmann, Kathleen Kennedy, Kevin Kennedy, S. Kennedy, J. Meisel, D. Nilov, S. Rajpurohit, N. Hultman (2022). “An ‘All-In’ Pathway To 2030: U.S. Methane Sector Emissions Reduction Potential.” Center for Global Sustainability, University of Maryland and America Is All In. 16 pp.

## Slide 63: Power
Transport
Methane

## Slide 64
Sectoral reductions to get to 52%
As of today, the U.S. has achieved 21% in reductions
From today’s levels, power sector contributes an additional 16%, transport sector contributes 5%, and methane sector contributes 3%.
Industry, buildings, lands, and other sectors contribute the remaining 5%
Notes: SAMPLE SLIDE +++++
DUPLICATE THIS SLIDE FOR THE NUMBER OF THIS TYPE YOU WILL NEED – ALWAYS HAVE ONE EXTRA
CHANGE HEADLINE OR SUBHEAD TEXT COLOR: Highlight text. Choose FORMAT SHAPE, then TEXT OPTIONS, then the first A. Keep black for the body text.

## Slide 65: US Model Comparison Study
Presented by Haewon McJeon

## Slide 66: Comparison of Participating Energy Systems Models
Abbr. | Model(s) | Institution | 2030 Emissions | Policies Assumed | Study
EDF-NEMS | RHG-NEMS | EDF | 51% net GHG reduction from 2005 | Suite of sector-specific policies and economy-wide limit on energy CO2 | Link
GCAM-USA-AP | GCAM-USA-AP | PNNL, CGS | 50% net GHG reduction from 2005 | Bottom-up, sector-specific suite of policies and incentives | Link
LBNL | FACT (transport), ReEDS+PLEXOS (power), EPS (other sectors) | UCB (FACT), NREL (ReEDS), Energy Innovation (EPS) | 50% GHG reduction from 2005 | 80% federal CES and no new gas in power sector 100% EV mandates for light-duty and 80% medium-/heavy-duty Building elec. mandates CH4/F-gas reductions | Link
PATHWAYS | RIO (supply-side), EnergyPATHWAYS (demand-side) | Evolved Energy Research | 53% net GHG reduction from 2005 | State and federal policies on the books as of Q3 2020 | Link
REGEN | US-REGEN | EPRI | 50% net GHG reduction from 2005 | Economy-wide CO2 cap by 2030 2035 electric sector net-zero target | Link
USREP-ReEDS | USREP-ReEDS | MIT, NREL | 50% CO2 reduction from 2005 | EE mandates 50% CO2 cap by 2030 | Link
Multi-model studies identify which insights are robust and which differ across models
Models assume different policy pathways to reach the 2030 target

## Slide 67: Working list of policies…
After the publication of the comparison paper, many new climate policies were enacted.
We’re continuously updating the policies to assess the emission impacts.

## Slide 68: Results: Sectoral Reductions to Reach 50x30 Targets
Chart: GHG Reductions by Sector (Mt-CO2e)
| 2019 | EDF-NEMS | GCAM-USA-AP | LBNL | PATHWAYS | REGEN | REGEN E+ | USREP-ReEDS | 2030 NDC
Electric | -782.1 | -1929.0375 | -2006 | -2059 | -2044 | -1916.207 | -1598.421 | -1846.7436
Industry | -32.0751 | -79.1515 | -220.6215 | -88.6215 | -186.1 | -79.7982 | -85.8955 | -564.5471
Buildings | 17.3 | -99.4178 | -178.8 | 26.2 | -96.8 | -93.729 | -132.7261 | -180.5088
Transport | -33.9765 | -380.5141 | -599.1 | -694.1 | -738.1 | -583.0191 | -857.5695 | -595.9459
Other CO2 | -47.8537 | -123.1664 | -327.5215 | -110.8804 | -110.8804
Non-CO2 GHG | 14.0194 | -343.3903 | -173.0096 | -285.5096 | -44.5096 | -322.1274 | -322.1274 | -80.8572
Sink | -1.1746 | -373.1614 | -152.9472 | -81.9472 | -211.9472 | -211.9472
Reduction from 2005 | -0.1305 | -0.50156 | -0.50196 | -0.46738 | -0.53037 | -0.50003 | -0.50031 | -0.49263
Electric
Buildings
Industry
Transport
Other CO2
Non-CO2 GHGs
Land
Notes
Bulk of reductions to reach 2030 target come from the electric sector and transport (~70-90% of 2030 reductions)
All sectors are involved to varying degrees: Halving GHGs is an “all-hands-on-deck” situation requiring many technology and policy tools
Source: Bistline, et al. (2022), “Actions for Reducing U.S. Emissions at Least 50% by 2030”

## Slide 69: What Could It Take? Rapid Buildout of the Grid
Historical maximum additions exceeded each year through 2030, but mix varies across models
Average build rate in scenario reaching 80% electric CO2 reduction by 2030
Chart: Capacity Additions (GW/yr)
| 1960 | 1961 | 1962 | 1963 | 1964 | 1965 | 1966 | 1967 | 1968 | 1969 | 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
Nuclear | 1.2374 | 2.0795 | 2.271 | 6.1771 | 4.0403 | 9.5243 | 6.4022 | 3.7755 | 6.8255 | 2.116 | 0.883 | 1.9285 | 4.3449 | 1.1257 | 3.304 | 7.871 | 8.4845 | 9.3724 | 7.5995 | 6.09 | 2.432 | 3.5749 | 1.195 | 1.123 | 1.122
Coal | 4.8954 | 3.675 | 3.7952 | 4.0096 | 4.4596 | 4.1398 | 3.353 | 6.7756 | 7.9696 | 11.2167 | 10.7198 | 12.1074 | 11.7825 | 14.4913 | 10.1908 | 10.7401 | 7.7425 | 10.9297 | 10.7298 | 9.7526 | 15.1763 | 8.8934 | 10.8511 | 6.1832 | 11.0615 | 6.1068 | 5.8589 | 4.0758 | 1.7911 | 3.3287 | 1.9211 | 3.1427 | 1.2675 | 0.1356 | 0.9495 | 2.522 | 1.2927 | 0.0782 | 0.0528 | 0.22 | 0.1215 | 0.44 | 0.011 | 0.0858 | 0.521 | 0.3994 | 0.5309 | 1.4189 | 1.4582 | 1.7863 | 5.3443 | 3.8303 | 3.734 | 1.5276 | 0.017
Wind | 0.0165 | 0.0185 | 0.0188 | 0.374 | 0.1502 | 0.1681 | 0.0976 | 0.1143 | 0.0266 | 0.0976 | 0.1045 | 0.0769 | 0.0065 | 0.0108 | 0.1244 | 0.03 | 0.019 | 0.1721 | 0.668 | 0.0612 | 1.5167 | 0.6668 | 1.6359 | 0.376 | 2.1622 | 2.6545 | 5.3 | 8.4848 | 9.9358 | 4.6742 | 6.8407 | 13.25 | 0.8644 | 4.9498 | 8.2383 | 8.7498 | 6.0625 | 6.8873 | 9.2672 | 14.6649 | 13.9836
Solar | 0.0148 | 0.03 | 0.073 | 0.036 | 0.0724 | 0.08 | 0.088 | 0.0001 | 0.0001 | 0.0046 | 0.003 | 0.0002 | 0.0029 | 0.0018 | 0.0999 | 0.034 | 0.1088 | 0.2354 | 0.7901 | 1.6071 | 3.5463 | 3.7657 | 3.5426 | 8.0067 | 5.1783 | 4.8922 | 5.5418 | 10.4376 | 13.1553
Storage | 0.002 | 0.001 | 0.04 | 0.003 | 0.006 | 0.013 | 0.0518 | 0.0718 | 0.0555 | 0.0307 | 0.1493 | 0.1871 | 0.124 | 0.2223 | 0.1684 | 0.4905 | 3.1439
Chart: 
| EDF-NEMS | GCAM-USA-AP | LBNL | PATHWAYS | REGEN | REGEN E+ | USREP-ReEDS
Gas | 1.5481 | 19 | 11.7794 | 20.8287 | 4.2825
Gas CCS | 3.6441 | 10.5 | 4.0294 | 0.27685 | 0.0233
Nuclear | 0 | 0
Other | 0.1 | 0.35223 | 0 | 2.3222
Wind | 5.0643 | 23 | 27.2 | 41 | 26.7284 | 19.9694 | 8.8631
Hydro | 0 | 0
Coal | 0 | 0
Solar | 43.0083 | 50 | 63.6 | 38 | 11.6094 | 9.0505 | 36.6935
Storage | 22.7 | 2 | 2.6272 | 1.1947 | 3.8384
EDF-NEMS
REGEN E+
Average Build Rate to 2030
REGEN
USREP-ReEDS
GCAM-USA-AP
LBNL
PATHWAYS
Gas CCS
Gas
Coal
Hydro
Other
Nuclear
Wind
Storage
Solar

## Slide 70: What Could It Take? Extensive Electric Vehicle Adoption
Chart: Electric Vehicle New Sales Share (%)
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Historical | 0.00011 | 0.00169 | 0.00407 | 0.00737 | 0.00891 | 0.00785 | 0.0102 | 0.01162 | 0.01973 | 0.01743 | 0.02041 | 0.040579
LBNL | 0.040579 | 0.5 | 1
GCAM-USA-AP | 0.040579 | 0.45 | 0.65
NEMS | 0.040579 | 0.1836 | 0.34
PATHWAYS | 0.040579 | 0.57
REGEN | 0.040579 | 0.162 | 0.452
REGEN E+ | 0.040579 | 0.586 | 0.745
USREP-ReEDS | 0.040579 | 0.36 | 0.93
LBNL
USREP-ReEDS
REGEN E+
GCAM-USA-AP
REGEN
EDF-NEMS
PATHWAYS
50x30
Reference
Average
Range
Biden 2030 target
EVs projected to reach 34-100% of new sales—10-25x current levels—which is much higher than with current policies and technology trends (i.e., “Reference” scenario)